## Slide 1
Solar Electric Technician Training (Level 2)
Presented By:
Module 3: Measurement of Electrical and Solar Parameters

## Slide 2
Basic Electrical Parameters

## Slide 3: Basics of Electricity- Voltage, Current & Resistance

## Slide 4: Basics of Electricity- Power & Energy

## Slide 5: Ohm’s Law

## Slide 6: Multimeter / Clamp-meter
Multi-meter
Clamp-meter

## Slide 7: Resistor Color Code Chart

## Slide 8: Ohm’s Law Relationship Between Voltage, Current & Resistance
Source : https://theengineeringmindset.com/ohms-law/

## Slide 9: Finding Voltage Example
Notes: Lets say we have a simple electrical circuit with a battery and a resistor. We don’t know what voltage the battery is though. The resistor is 3Ω and when we connect a multimeter into the circuit we see that we get a reading of 2 Amps.

## Slide 10: Ohm‘s Law Relationship Current & Voltage
Notes: if we double the voltage by connecting two 6V batteries in series, we get 12V. If we now connect this to the same circuit, the current also doubles from 2A to 4A. If we double the voltage again to 24V the current will also double to 8A.

## Slide 11: Finding Current Example
Notes: Lets say we now have a 3Ω lamp connected to a 6V power supply. To find the current we write down I = and cover up the I in the triangle. That gives us V ÷ R so Current equals Voltage divided by resistance. We know the voltage is 6V and the resistance is 3 ohm so the current is therefore 2A and that’s what we see with the multimeter.

## Slide 12: Ohm‘s Law Relationship Current & Resistance
Notes: So we saw what happens when we use a resistance of 3 ohms in the circuit. But If we double the resistance to 6 ohms by placing another 3 ohm lamp into the circuit, the current halves to 1A.
If we double the resistance again to 12 Ohms, the current will half again to 0.5A. We can visually see this because the lamps will become less bright as the current reduces from the increase in resistance.

## Slide 13: Finding Resistance Example
Notes: Say we have a resistive lamp connected to a 12V power supply. We don’t know how much resistance it’s adding to the circuit but we measure the current as 0.5 A.
To find resistance we write down R = and cover up the R on the triangle. We’re left with V and I so Resistance = Voltage divided by current. We know the voltage is 12V and the current is 0.5A so 12 divided by 0.5 gives us 24 Ohms of resistance.

## Slide 14: Finding Resistance Example

## Slide 15: Finding Resistance Example
Notes: So given a circuit, we can increase the current by increasing the voltage or we can also increase the current but reducing the resistance. We can also reduce the current by increasing the resistance.

## Slide 16: Test Skills - Problem 1
Notes: I = V ÷ R I = 120V ÷ 240 Ω I = 0.5A

## Slide 17: Test Skills - Problem 2
Notes: V = I x R V = 0.958A x 240Ω V = 229.9V (~230V)

## Slide 18: AC and DC voltage

## Slide 19: AC and DC current

## Slide 20: Single Phase and Three Phase Power Supply

## Slide 21: Single Phase Distribution Box Wiring and Connection Procederes
Click on the link provided to get detailed procedures
https://www.etechnog.com/2023/04/single-phase-distribution-box-db-wiring.html

## Slide 22: Three Phase Distribution Box Wiring and Connection Procedures
Click on the link provided to get detailed procedures
https://www.etechnog.com/2023/04/three3-phase-distribution-board-wiring.html

## Slide 23: Three Phase Distribution Box Wiring and Connection Procedures
Click on the link provided to get detailed procedures
https://www.etechnog.com/2023/04/three3-phase-distribution-board-wiring.html

## Slide 24: DC Power Supply

## Slide 25: AC Power Supply

## Slide 26: Bypass diode

## Slide 27: Bypass and Blocking diode

## Slide 28
Electrical Connections: Series and Parallel

## Slide 29: Series and Parallel Connection

## Slide 30: Series and Parallel Connection

## Slide 31: Series and Parallel Connection

## Slide 32: Continuity Test

## Slide 33: Earth Resistance
5 ~ 10 m
5 ~ 10 m
Auxiliary Earth Spike
Earthed Electrode under Test